Hive Selection Application

Specifications
1. General purpose:
This application is designed to get patients items from a hive of sorted items. Each item	would	be marked with an ID on the front of the box in which its in ,via an apriltag, and for	each type of item, the number of apriltags in the relevant box would match the number of	items inside. The robot should approach the hive, select a box which contains the relevant i	tem, check if that item is in stock, and if it is, take it, and deliver it to the patient.

Software Substasks
1.1 Receive a command from the fleet / ui to grab item X and go to room Y.
1.2 Navigate to the hive.
1.3. Detect the apriltags on the hive.
1.4. Look for the apriltag matching the ID of the selected item.
1.5. Approach the relevant tag.
1.6. Check that the selected item is in stock.
1.7. Grab the selected item.
1.8 Move away from the hive.
1.9 Deliver the item to the patient.

Mechanical Subtasks
2.1 Build a real size hive model

Schedule
13.11 – 23.11
(1.3 + 1.4) Detect the apriltags on the hive and look for the relevant apriltag
1.3.1 – Detect the point in space (x,y,z,θ) of every frontal apriltag.
Required: Calibrated cameras

2.1 Build a real size model
2.1.1 - Design and create real size model to match the exact measurements of the hive to be	used for the application.
Required:
A premilinary testing of (1.3 + 1.4) to estimate real life hive measurements.
A consult with the mechanical team on how to build, what materials to use, and expected	time of the hive to be ready.

1.5 Approach the relevant tag
1.5.1 - Approach the relevant tag, a predefined distance away on the y axis (frontal axis).
1.5.2 – Minimize positioning errors to be within the predefined constraints that are chosen	by the user.
Required: Enhancment of the ApproachToSomething skill to add the predefined y axis	distance, and correction of the positioning errors that are larger than the constraints that can	be defined in the skill.

1.6 Check that the selected item is in stock
1.6.1 – Check that the item is in stock via the number of remaining apriltags in the box.
Required: A real life size hive model (will be provided by 2.1).

24.11 – 3.12
1.7 – Grab the selected item
1.5.1 – Place the arm infront of the relevant box.
1.5.2 – Move the arm inside of the box, to the item.
1.5.3 – Grab the item (close the gripper).
1.5.4 – Move the arm back outside.
1.5.5 – Position the arm in a carrying position.
Required: Calibrated arms and physical feedback. At this point it’d also be good to have	arms accuracy such that a tailored calibration would not be required, and the app would	be able to work with every arm, of every robot. At the moment, for each robot the	calibration offset is found manually	and is then corrected, upon every calibration. These	issues should be resolved once the servo and force sensors features are provided. For the	moment, the app will be built considering those limitations.

1.8– Move away from the hive
1.6.1 – Move backwards, turn 180 degrees.

1.9 – Deliver the item to the patient
1.7.1 – Navigate with the item to the patient, and place it on either a designated table, or an	empty part of the bed
Required: Mapping the relevant space, working navigation systems.

** In my opinion, basing the entire application on tag detection would pose problems in a real life environment. If and when we face these problems, I suggest an object detection model for the relevant items, so that the arm movements would not be based soley on constants.